## Slide 1: 망고100 보드로 놀아보자-15
UART,Keypad,이더넷 드라이버
안드로이드에서 키 처리
http://cafe.naver.com/embeddedcrazyboys

## Slide 2: DEBUG PORT 포팅
$(topdir)./config 파일에서
CONFIG_S3C_LOWLEVEL_UART_PORT=1
# CONFIG_SPLIT_ROOT_FILESYSTEM is not set
Kernel configuration에서
“kernel hacking-> S3C UART to use for low-level debug “
에서 1 선택
./arch/arm/plat-s3c/include/plat/uncompress.h 소스에 포함
#define uart_base S3C_PA_UART + (S3C_UART_OFFSET * CONFIG_S3C_LOWLEVEL_UART_PORT)
.dev_name = "s3c2410_serial",
./drivers/serial/samsung.c 에서 디바이스 이름을 수정 할 수 있습니다.

## Slide 3: LCD 드라이버 수정-1
#make menuconfig
“Device Drivers->Graphic Support
->Support for frame buffer devices
->S3C Framebuffer support 선택

## Slide 4: LCD 드라이버 수정-2
void lcd_power_ctrl(s32 value)
{
int err;
if (value) {
if (gpio_is_valid(S5PC1XX_GPH0(2))) {
err = gpio_request(S5PC1XX_GPH0(2), "GPH0");
if (err) {
printk(KERN_ERR "failed to request GPH0 for "
"lcd reset control\n");
}
gpio_direction_output(S5PC1XX_GPH0(2), 1);
}
}
else {
if (gpio_is_valid(S5PC1XX_GPH0(2))) {
err = gpio_request(S5PC1XX_GPH0(2), "GPH0");
if (err) {
printk(KERN_ERR "failed to request GPH0 for "
"lcd reset control\n");
}
gpio_direction_output(S5PC1XX_GPH0(2), 0);
}
}
gpio_free(S5PC1XX_GPH0(2));
lcd_power = value;
}
./drivers/video/samsung/s3cfb_lte480wv.c
에서 lcd_power_ctrl함수를 수정
LCD 에 전원을 인가한다.

## Slide 5: LCD 드라이버 수정-3
static struct s3cfb_lcd lte480wv = {
.width = 800,
.height = 480,
.bpp = 24,
.freq = 60,
.timing = {
.h_fp = 8,
.h_bp = 13,
.h_sw = 3,
.v_fp = 5,
.v_fpe = 1,
.v_bp = 7,
.v_bpe = 1,
.v_sw = 1,
},
.polarity = {
.rise_vclk = 0,
.inv_hsync = 1,
.inv_vsync = 1,
.inv_vden = 0,
},
};
drivers/video/samsung/s3cfb_lte480wv.c
에서 LCD datasheet 타이밍만 맞추면 됨

## Slide 6: LCD 드라이버 수정-4
static int s3cfb_init_global(void)
{
fbdev->output = OUTPUT_RGB;
fbdev->rgb_mode = MODE_BGR_P;
fbdev->wq_count = 0;
init_waitqueue_head(&fbdev->wq);
mutex_init(&fbdev->lock);
s3cfb_set_output(fbdev);
s3cfb_set_display_mode(fbdev);
s3cfb_set_polarity(fbdev);
s3cfb_set_timing(fbdev);
s3cfb_set_lcd_size(fbdev);
return 0;
}

## Slide 7: 이더넷 드라이브 포팅-1
static struct resource s3c_smsc911x_resources[] = {
[0] = {
.start = S5PC1XX_PA_SMSC9220,
.end = S5PC1XX_PA_SMSC9220 + SZ_1M - 1,
.flags = IORESOURCE_MEM,
},
[1] = {
.start = IRQ_EINT11,
.end = IRQ_EINT11,
.flags = IORESOURCE_IRQ,
},
};
arch/arm/plat-s5pc1xx/devs.c 에서 수정
#define S5PC1XX_PA_SMSC9220 (0xA0000000)
/arch/arm/mach-s5pc100/include/mach/map.h

## Slide 8: 이더넷 드라이버 포팅 -2
“Device driver->Network Device support에서 선택
Configuration 파일 drivers/net/Kconfig 위치

## Slide 9: 이더넷 드라이버 -3
./arch/arm/mach-s5pc100/mach-mango100.c
디바이스 등록 소스는
./arch/arm/plat-s5pc1xx/devs.c
에 위치

## Slide 10: 이더넷 디바이스 확인 방법

## Slide 11: 이더넷 드라이버 확인 방법

## Slide 12: 이더넷 드라이버 irq 등록확인
S5pc100 user manual에는 11번째에
EINT11이다, 근데 등록은 32를 더한 값인
43번째 등록이 되어 있다.
이유는 커널이 32번까지 spurious
인터럽트로 등록하여 사용한다.
#define IRQ_EINT11 S5PC1XX_IRQ_VIC0(11)
./arch/arm/plat-s5pc1xx/include/plat/irqs.h

## Slide 13: Keypad driver
./driver/input/keyboard/Kconfig 에 추가
.config 파일에
CONFIG_KEYPAD_MANGO100_LINUX_EVENT=y

## Slide 14: Keypad driver
./driver/input/keyboard/ 파일을 추가한다.
./driver/input/keyboard/Makefile 에 추가

## Slide 15: Keypad driver
Driver/input/keyboard/mango100-keypad.c
등록확인은 아래와 같이 확인 할 수 있다.

## Slide 16: Keypad driver
struct input_event {
struct timeval time;
__u16 type;
__u16 code;
__s32 value;
};
./include/linux/input.h에 정의
#define EV_KEY 0x01
#define KEY_BACK 158 /* AC Back */
키를 누르면 value값은 1을 가진다
# hexdump /dev/input/event0
Key 누를경우
Key Release

## Slide 17: Keypad driver
mango100_keypad.driver->name = DEVICE_NAME;
mango100_keypad.driver->phys = "mango100-keypad/input0";
mango100_keypad.driver->open = mango100_keypad_open;
mango100_keypad.driver->close = mango100_keypad_close;
mango100_keypad.driver->id.bustype = BUS_HOST;
mango100_keypad.driver->id.vendor = 0x16B4;
mango100_keypad.driver->id.product = 0x0701;
mango100_keypad.driver->id.version = 0x0001;
# cat /proc/bus/input/devices
I: Bus=0019 Vendor=16b4 Product=0701 Version=0001
N: Name="mango100-keypad"
P: Phys=mango100-keypad/input0
S: Sysfs=/class/input/input0
U: Uniq=
H: Handlers=kbd event0
B: EV=3
B: KEY=40000800 0 0 0 0
./drivers/input/keyboard/mango100_keypad.c 소스에 mango100_keypad_prob함수에 정의
#define BUS_HOST 0x19
./include/linux/input.h

## Slide 18: Keypad driver
“Kernel hacking “ 설정
CONFIG_TIMER_STATS=y 로 설정
# echo 1 > /proc/timer_stats
# cat /proc/timer_stats
Timer Stats Version: v0.2
Sample period: 2.911 s
291, 1 swapper mango100_keypad_config (mango100_rd_timer_handler)
2, 1 swapper schedule_delayed_work_on (delayed_work_timer_fn)
8, 1867 er.ServerThread futex_wait (hrtimer_wakeup)
3, 1 swapper phy_start_machine (phy_timer)
3, 1832 zygote queue_delayed_work (delayed_work_timer_fn)
1, 0 swapper page_writeback_init (wb_timer_fn)
308 total events, 105.805 events/sec
To activate the collection of stats
# echo 0 > /proc/timer_stats
To stop collecting stats

## Slide 19: Keypad driver flow
mango100_keypad.rd_timer
mango100_rd_timer_handler
mango100_keypad_control
GET_KEYPAD_DATA
generate_keycode
input_report_key
에서 이벤트 발생
10ms 마다 스캔
Button (Hardware)

## Slide 20: 안드로이드 Key event 처리
Key button Map 정의는 vendor\sec\mango100\mango100-keypad.kl
frameworks/base/libs/EventHub.cpp에 scan_dir,open_device 정의
static const char *device_path = "/dev/input";
bool EventHub::openPlatformInput(void)
{
..
res = scan_dir(device_path);
..
}
int EventHub::open_device(const char *deviceName)
KeyInputQueue( 1853): InputDeviceReader.run()
int EventHub::scan_dir(const char *dirname)
{
while((de = readdir(dir))) {
strcpy(filename, de->d_name);
open_device(devname);
}
}

## Slide 21: 안드로이드 Key event 처리
export ANDROID_ROOT /system
/init.rc에 정의
int EventHub::open_device(const char *deviceName)
{
…
const char* root = getenv("ANDROID_ROOT");
property_get("persist.sys.keylayout", keylayout, "qwerty");
snprintf(keylayoutFilename, sizeof(keylayoutFilename),
"%s/usrkeylayout/%s.kl", root, keylayout);
strcpy(devname, keylayout);
bool defaultKeymap = access(keylayoutFilename, R_OK);
if (defaultKeymap) {
snprintf(keylayoutFilename, sizeof(keylayoutFilename),
"%s/usr/keylayout/%s.kl", root, "qwerty");
strcpy(devname, "qwerty");
}
LOGI("2:devname = %s, keylayout =%s, keylayoutFilename = %s",
devname, keylayout, keylayoutFilename);
device->layoutMap->load(keylayoutFilename);
….
}
I/EventHub( 1853): 2:devname = qwerty,
keylayout =qwerty,
keylayoutFilename = /system/usr/keylayout/qwerty.kl
-#logcat 명령으로 디버깅 메시지 출력
frameworks/base/libs/ui/EventHub.cpp파일에
EventHub::open_device함수에 정의

## Slide 22: 안드로이드 Key event 처리
int EventHub::open_device(const char *deviceName)
{
…
LOGI("New keyboard: publicID=%d device->id=0x%x devname='%s' propName='%s' keylayout='%s'\n",
publicID, device->id, name, propName, keylayoutFilename);
}
LOGI("New device: path=%s name=%s id=0x%x (of 0x%x) index=%d fd=%d classes=0x%x\n",
deviceName, name, device->id, mNumDevicesById, mFDCount, fd, device->classes);
LOGV("Adding device %s %p at %d, id = %d, classes = 0x%x\n",
deviceName, device, mFDCount, devid, device->classes);
}
frameworks/base/libs/ui/EventHub.cpp 에 open_device 정의
#logcat 명령으로 출력 결과
I/EventHub( 1853): New keyboard: publicID=65537 device->id=0x10001
devname='mango100-keypad' propName='hw.keyboards.65537.devname' keylayout='/system/usr/keylayout/qwerty.kl'
I/EventHub( 1853): New device: path=/dev/input/event0 name=mango100-keypad id=0x10001 (of 0x2) index=2 fd=58 classes=0x1

## Slide 23: 안드로이드 Key event 처리
Thread mThread = new Thread("InputDeviceReader") {
public void run() {
if (DEBUG) Log.v(TAG, "InputDeviceReader.run()");
android.os.Process.setThreadPriority(
android.os.Process.THREAD_PRIORITY_URGENT_DISPLAY);
RawInputEvent ev = new RawInputEvent();
while (true) {
try {
InputDevice di;
// block, doesn't release the monitor
readEvent(ev);
boolean send = false;
boolean configChanged = false;
if (true) {
Log.i(TAG, "Input event: dev=0x"
+ Integer.toHexString(ev.deviceId)
+ " type=0x" + Integer.toHexString(ev.type)
+ " scancode=" + ev.scancode
+ " keycode=" + ev.keycode
+ " value=" + ev.value);
}
Key Event 처리 Thread
#logcat 메시지
I/KeyInputQueue( 1853): Input event:
dev=0x10001 type=0x1 scancode=158
keycode=4 value=1
Mango100-keypad.kl과 scancode값 일치
BACK 키 수행이 됨
./frameworks/base/services/java/
com/android/server/KeyInputQueue.java
파일에 정의

## Slide 24: 안드로이드 Key event 처리
Thread mThread = new Thread("InputDeviceReader") {
…..
while (true) {
try {
InputDevice di;
// block, doesn't release the monitor
readEvent(ev);
……
frameworks/base/services/java/com/android/server/KeyInputQueue.java
frameworks/base/services/jni/
com_android_server_KeyInputQueue.cpp

## Slide 25: 안드로이드 Key event 처리
public final boolean dispatch(Callback receiver, DispatcherState state,
Object target) {
switch (mAction) {
….
case ACTION_UP:
if (DEBUG) Log.v(TAG, "Key up to " + target + " in " + state
+ ": " + this);
if (state != null) {
state.handleUpEvent(this);
}
return receiver.onKeyUp(mKeyCode, this);
public void handleUpEvent(KeyEvent event) {
final int keyCode = event.getKeyCode();
if (DEBUG) Log.v(TAG, "Handle key up " + event + ": " + this);
#logcat 수행 결과
KeyEvent( 1910): Key up to android.inputmethodservice.InputMethodService$InputMethodSessionImpl@43da0b40 in
android.view.KeyEvent$DispatcherState@43d92cf8: KeyEvent{action=1 code=4 repeat=0 meta=0 scancode=158 mFlags=8}
V/KeyEvent( 1910): Handle key up KeyEvent{action=1 code=4 repeat=0 meta=0 scancode=158 mFlags=8}: a
ndroid.view.KeyEvent$DispatcherState@43d92cf8
D/MountListener( 1853): handleEvent ums_connected
./frameworks/base/core/java/android/view/KeyEvent.java
에서 dispatch를 한다.

## Slide 26: 안드로이드 Key Event 처리
Window Manager
distpatchKey(KeyEvent..)
frameworks/base/services/java/com/android/server/WindowManagerService.java
Thread mThread = new Thread("InputDeviceReader")
readEvent(ev);
di = newInputDevice(ev.deviceId);
frameworks/base/services/java/com/android/server/KeyInputQueue.java
static JNINativeMethod gInputMethods[] = {
/* name, signature, funcPtr */
{ "readEvent", "(Landroid/view/RawInputEvent;)Z",
(void*) android_server_KeyInputQueue_readEvent },
frameworks/base/services/jni/com_android_server_KeyInputQueue.cpp
static const char *device_path = "/dev/input";
bool EventHub::getEvent(int32_t* outDeviceId, int32_t* outType,
bool EventHub::openPlatformInput(void)
frameworks/base/libs/ui/EventHub.cpp